## Slide 1
Pintor Ortiz Walter Frank
Vijay Yadunund
ARTC
ARA Digitalization - HS&E and Process Quality Enhancement through IIoT
26 June 2019
3.0

## Slide 2: Revision History
Version | Version Date | Section | Details of Revision
2.0 | 15/03/2019 | N.A. | Initial draft
3.0 | 25/06/2019 |  | Development

## Slide 3: Contents
Project Definition
  Problem Statement
  Project Objectives
  Technical Requirement
Project Plan
  Work Breakdown Structure
  Proposed Methodology
  Project Schedule
  Key Milestones
  Project Deliverables
Project Management
  Risks & Mitigations
  RACI Chart
  Stakeholders Map
  Communication Plan
Miscellaneous
  Questions about the project
  Project Costs
  Project Intellectual Property

## Slide 4: Problem Statement
Currently at ARTC, there is no defined structure (both hardware and software) to obtain key information from robotic industrial environment where processes are executed (Robotic cells). There are efforts to retrieve information (such as joint values, robot position, etc.) from robot controllers, but a more flexible and industry-ready solution needs to be adopted (Creation/implementation of a platform). Insufficient information will lead to unsafe and uncertain scenarios in the future. Obtaining the right information will lead to solve current issues, such as:
Inexact utilization of power/resources (Robot operation, external actuators, lights)
Definition of dangerous environments for operators (Dust levels for instance)
Temperature changes (Process instability)
Environment vibrations
Notes: Robotic environment data can be retrieved and published to cloud services to facilitate monitoring.

## Slide 5: Project Objectives & Scope
This project aims at developing an IoT framework to understand robotic operating status, safety levels an other crucial robot information to enable digitalization capabilities.
In-Scope
Selection of IIoT solution
Sensors selection and integration in robotic cell
Sensors data streaming and monitoring
  Data collected includes dust levels, humidity/temperature, noise levels and relevant variables for environment monitoring
Robots data streaming and monitoring
  Data collected includes robots pose frame, joint values, robot state and select IO signals only
Robot Data streaming using TCP/IP protocol
Out of Scope
Application support for brands other than ABB
Visualization/Simulation of robots
Encryption of data accessed
Benchmarking of calibration results against similar applications
Commercialization

## Slide 6: Technical Requirement
Robotic industrial setups are lacking key information.
  Process set-up – Process information and environmental effects on process
    Information of physical devices to generate digital twins
    Optimization of processes by monitoring and standardization (humidity/temp)
  HS&E – Optimal conditions (environment) for humans to interact
  Energy consumption – Extended hours of utilization
Notes: https://sg.element14.com/sharp/gp2y1010au0f/sensor-dust-optical/dp/9707956?gclid=Cj0KCQjws5HlBRDIARIsAOomqA2EnFvCT2uMoDfKBz0SxB2m9h0-YPvDkxKXRRPkkt4y32VpwxpocRAaAiddEALw_wcB&gross_price=true&mckv=sdPSduIJG_dc|pcrid|155925702681|pkw||pmt||slid||product|9707956|pgrid|34507690943|ptaid|pla-41477300408|&CAWELAID=120185760001223203&CAGPSPN=pla&CAAGID=34507690943&CMP=KNC-GOO-SHOPPING-9707956&CATCI=pla-41477300408

## Slide 7: Proposed Methodology
Data extraction
Connectivity
Data streaming
Objectives: Collect all data and information, from both robot controller and industrial robotic environment.
Scope:
(1) Sensor selection
(2) Sensor integration and strategic placement
Methodology:
(1) Design conceptualization and selection
(2) Sensor knowledge and characterization
Objectives:
Low level sensors and robot controllers pass information to the industrial PC
Scope:
(1) Robot controller software for data collection – TCP/IP
(2) Robotic environment data collection - UART
(3) Robot controller software for data streaming – TCP/IP
Methodology:
(1) Develop software modules for TCP/IP communication
(2) Test and debug software
Objectives:
Bridge the existing gaps between IPCs and Clouds to ensure the correct flow of data.
Scope:
(1) Local server to collect robot controller data
(2) OPC-UA integration between IPC, Gateway and Cloud
(2) Data visualization through tools like tableu
Methodology:
(1) Develop software modules for OPC-UA communication
(2) Develop Graphical User Interfaces for data visualization
(2) Test and debug software

## Slide 8: Proposed Methodology
Integration of IIoT concepts:
  Sensor selection and integration to IPC
  Data extraction and collection / Data streaming to cloud services
  Data visualization / Dedicated dashboard
Development of software applications for robot data retrieval with GUI to:
  Connectivity between robot controllers and PC application. The system will be able to:
    Read robot pose frames, joint values, robot state and select IO signals
    Define format for packing data prior to publishing. The same format to be used for unpacking at destination
    Publish data to remote server via TCP/IP connection
ABB IRC5 (1)
TCP/IP
ABB IRB
IPC
* Example of environment monitoring and process control.
OPC-UA
Gateway / Ex. Mindconnect nano
To Cloud
UART/An In
ABB IRC5 (2)
UART/An In
ABB IRB

## Slide 9: Proposed Methodology
Field Site
Edge Intelligence
Cloud Management
EIS
EIS
Sensor
USB-4704
Cloud Integration
EVM Insight Dashboard
3rd party
Sensor
*Example of system diagram – Courtesy of Advantech
Target area

## Slide 10: Work Breakdown Structure
System architecture, GUI design, application wireframes
Network Scanner to scan and connect to robot controllers in the network
Project updates
Read/Write RAPID data
Format Data packaging
Publish packaged data
IPC to Gateway connectivity
Digitalization for ARA team (IIoT) – HS&E and Process Quality Enhancement through IIoT
Robotic Environment – Data extraction
Robot Controller -Data extraction
Connectivity
Report
Gateway to Cloud connectivity
Performance evaluation
Dashboard and data visualization development
Data extraction
Sensor selection
Sensor Integration
Lessons learnt
Report writing
Data streaming
Sensor Characterization

## Slide 11: Project Schedule
 |  | May |  |  |  |  | June |  |  |  | July |  |  |  |  | August |  |  |  |  | 
 |  | W1 | W2 | W3 | W4 | W5 | W1 | W2 | W3 | W4 | W1 | W2 | W3 | W4 | W5 | W1 | W2 | W3 | W4 |  | 
Project initiation | PA and documentation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Design and initial concept |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Planned
 | RA |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | On execution
 | Kick-off session |  | M0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Data Extraction - Robotic environment | Sensor Selection (Procument included) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Sensor Integration |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Sensor Characterization |  |  |  |  |  | M1 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Data Extraction - Robot controller | Development of functions to access controller |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Network Scanner - ABB Robots |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Read/Write RAPID |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Communication (Data format and publishing of data) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | GUI design |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Evaluation, debugging and testing |  |  |  |  |  |  |  |  |  | M2 |  |  |  |  |  |  |  |  |  | 
Connectivity | IPC to Gateway connectivity |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Gateway to Cloud connectivity |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Dashboard and data visualization |  |  |  |  |  |  |  |  |  |  |  |  |  |  | M3 |  |  |  |  | 
Final Report | Report preparation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Report review (ARTC) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Report release |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | M4 |  | 

## Slide 12: Key Milestones
Project start – May 2019
M1: Sensors integration / Environment – June 2019
M2: Evaluation, debugging and testing / Robot – July 2019
M3: Dashboard and data visualization – August 2019
M4: Report – August 2019

## Slide 13: Project Deliverables
Hardware environment
  Sensors to identify physical environments in the network
  Hardware Integration
Software executables for
  Data Streaming
  IPCs and Gateway connectivity
  Dashboard
A report that covers the following:
  Software architecture
  Hardware structure
  Development methodology
  Results

## Slide 14: Hardware Environment
Sensors to identify physical environments (Still being selected)
Example – SaintSmart flame detection sensor
XDK – 8 Sensors in 1
Immersion temperature reader
CISS – Bosch Sensors

## Slide 15: Hardware Environment
Other hardware (Acquired)
Industrial PC - Edge
IO acquisition cards – AIO (4-20mA – 0-5v – 0-10v) / DIO
Routers

## Slide 16: Software
Data streaming for ABB robot controller
1
2
3
4
Controllers in network
Options to read
Data displayed
Server information to be published using the standard TCP/IP protocol
C#

## Slide 17: Software
Example of operation for Robotic Data Streamer

## Slide 18: Software
IIoT_Robotics and Robot_broadcaster
TCP/IP server IP address
Displaying boxes for data received from TCP/IP client
Variables declaration for IPC (OPC-UA server)
1
2
3

## Slide 19: Software
Example of operation for IIoT_Robotics and Robot_broadcaster
Python
Structured Text => PLC

## Slide 20: Software
Dashboard concept
1
2
3
Robot Joint chart
Robot data
Gauges for general information about working cell – To be increased

## Slide 21: Software
Dashboard

## Slide 22: Next steps
Hardware
Finalize procurement of sensors
Integration
Integrate/connect robot controller(s) in same network
Software
Characterization of sensors
Ensure initialization of robot streamer connects to all robots in network
Connection of multiple robots in robot streamer
  Stream quantity of ABB robots connected
  Robot_broadcaster to receive and publish more information
  Investigate if OPC-UA server can autonomously generate new variables for robots and sensors
    If not possible, define the bandwidth for operation in ARTC

## Slide 23: High Level Risks & Mitigations
ID | Risk Description | Initial Risk |  |  | Mitigation Plan | Mitigated Risk |  |  | Owner
 |  | Likelihood | Impact | Risk Level |  | Likelihood | Impact | Risk Level | 
1 | Connectivity issues among nodes and gateway | 3 | 4 | 12 | Utilize initially simple protocols of communication to demonstrate IoT | 2 | 4 | 8 | Walter
2 | Connectivity issues between digital suite and server | 3 | 2 | 6 | Utilize same host machine | 3 | 2 | 6 | Yadunund
3 | Limitations of sensors to detect physical variations | 1 | 5 | 5 | Identify zones of risks Utilize more sensitive sensors | 1 | 4 | 4 | Walter

## Slide 24: RACI Chart
 | Project Management | Project Team Members | 
 | Project Manager | Vijay Yadunund | Pintor Ortiz Walter Frank
Project Capture |  |  | 
Receipt of SoW/SoR |  | A | R
Project Charter Preparation and Approval |  | A | R
Project Initiation |  |  | 
Scoping pack, Cost Sheet and Project Agreement preparation |  | A | R
Project Execution |  |  | 
Software Architecture and application wireframes |  | R | R
Network scanning and connectivity framework |  | R | C
Passive data access module |  | R | C
Data packing format |  | C | R
Plane fitting algorithm |  | R | C
Sphere fitting algorithm |  | C | R
Laser scanner integration |  | R | C
Software integration |  | R | C
Testing |  | R | R
Project Closure |  |  | 
Final Report |  | R | C
Project Closure meeting |  | R | R

## Slide 25: Stakeholders Map (Projects w/o RI/IHL and Customers )
Escalation Path
ARTC
<Name> (Project Manager)
Pintor Ortiz Walter Frank(Technical Leader)
Vijay Yadunund (Team Member)
ARTC
David Low (Chief Executive Officer)
Nicholas Yeo (Technical Director)
Chia Kiang Sum (PMO Director)
ARTC
Tijo Thayil (Group Manager)

## Slide 26: Communication Plan
Kick-off Meeting
  Involving all Project Members and Stakeholders after the project is approved and bought-off
Weekly Team Meetings
  Discussions on project updates and issues with <Member company> Project Managers
Fortnightly Meetings with Sponsor
  Review of project updates with all Stakeholders via emails/WebEx
Closing Meeting with Sponsor
  Review of project delivery with all Stakeholders via emails/WebEx once project is confirmed to be completed

## Slide 27: Questions about the Project
No. | Question | Owner | Answer
1 | <List of questions to the stakeholders raised during project scoping phase> | <Person responsible of answering the question> | <Answer to question>
2 |  |  | 
3 |  |  | 
4 |  |  | 

## Slide 28: Project Intellectual Property
Background IP (Contributions to the Project) | 
ARTC Owned | Member Owned
Intellectual Property (e.g. Pending/granted patents, designs, trade secret, etc.) | Intellectual Property
Technology (e.g. Know-how, experience, processes, etc.) | Technology
Foreground IP (Expected Outcomes)
Deliverables
Software applications for passive data streaming, workobject and tooldata calibrations
Intellectual Property
Technology
Insert more rows if required
Proposed FIP Ownership | 
Schedule 5 | ARTC Owned
Delete Row as appropriate